## Slide 1
Hussam Abdellatif | Ph.D. Candidate Master Thesis Defense – July 2025
Advisor: Dr. Josep M. Jornet
Committee: Dr. Dimitrios Koutsonikolas, Dr. Testolina, Paolo
Microwave Based Wireless Communication for NTN: A Thorough Investigation Using Simulation Based Model

## Slide 2: NTN: Utilizing Satellite Networks For Wireless Communication
Candidates For High-Speed Links (UL,DL,CL)
mmWave - [Ka, V] Offers a balanced trade-off between bandwidth, transmission distance, and alignment requirements.
THz Provides extremely high bandwidth, but with moderate range and more demanding alignment precision.
Optics Delivers the highest bandwidth, but demands precise alignment and is sensitive to atmospheric conditions
180
1500
0.1
0.01
Notes: This presentation is split into 2 categories:
Physical Layer
MAC Layey
Two essential elements in the OSI Stack ..
In terms of the physical Layer we present 2 solutions:
Hyprid
  Digital Domain imp
  The PHY layer
  The Analog Domain
Digital {Future Work}
  High Speed D/c
  Digital Impl.
MAC
  Utilizing reflective Surfaces for NLoS

## Slide 3: NTN: Motivation Behind Satellite Based Communication
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
Latency
LEO massive constellations allow for wireless based networks
  Dynamic/Robust
  Wireless Based Links [Routing]
  Less Congestion
Global Coverage
Large constellations allow for more global coverage:
  Remote/Rural Areas
  Damaged Ground Infrastructure [emergencies]
Throughput
Channel/Link condition allow for high frequency usage
  Access to more bandwidth
  Less Congestion
  Frequency Reuse
Service Cost
Satellite constellations can serve more users
  Lower Service Cost at Scale
  Unified NW Provider [Global]
Notes: Backbone maps: Mapping the Internet - ITGS News

## Slide 4: NTN: Simulators*
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
* Disclaimer: This Project Was Completed in 2020. At the time, STK was the main (and one of very few) satellite simulator
STK: Systems Tool Kit
NS-3 LEO Extension
Satellite Toolbox
Released On 1989
Industry Standard For Satellite Simulations/Analysis
License Required ($$$)
Complex Tool
Not Open-Source
Difficult To Adapt In Research Settings
Released On 2022
Built on Top of NS-3
C++ [not a dominant language in research]
Contains Vast Communication-Based Modules/Ips
Free/Open-Source
Released On ~2021
MATLAB Based
Less Learning Curve
Simple and Powerful

## Slide 5: Our Work: In-House NTN Simulator
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
Goal
Develop an NTN Simulator
    Fully Capture Satellite Characteristics
      Orbital Parameters
      Real-Time Movement/Orientation
      Field of View
Develop NTN Based Link Budget
    mmWave
    THz Band
Satellite Constellations and Routing
TLE
Notes: An All-Programmable 16-nm RFSoC for Digital-RF Communications | IEEE Journals & Magazine | IEEE Xplore

## Slide 6: Simulator Architecture
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
Simulation
Environment
Load Satellite Constellation From TLE
Setup Ground Stations
Setup Timing
Compute Satellite Orbital Parameters (for each Satellite)
Grab Weather Conditions From API For Each Ground Station
Setup RF Parameters and Channel
Begin Simulation
Loop Over Generated Transmission Instances
Compute Satellite Coordinates
Find Suitable UL LINK
[GS  SAT]
Find CL Route
[SAT  SAT]
Find Suitable DL LINK
[SAT  GS]
Compute Satellite CL [shortest hop]
Compute SNR, Data Rate, Latency
time [i]

## Slide 7: Orbital Parameters
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
  Length of Semi-Major Axis: Half of the longest diameter of an elliptical orbit
  Eccentricity: The shape of the orbit (Ellipse  Circle)
  Ture Anomaly: Angle between the direction of periapsis (shortest line segment to earth) and the current position of the satellite
  Eccentric Anomaly: Angle between the center of the ellipse and a point on the circumference of a circumscribed circle
  Mean Anomaly: Time since the last crossing of periapsis
Extracted From TLE or Generated From Scratch For Custom Satellite Constellation
Notes: r = distance from the focus to the satellite
tp is the time since the last crossing T is the orbital period of the satellite.

## Slide 8: Satellite Tracking
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
  Compute Instantaneous Time (past, present, future):
    Convert Time to UTC standard timing and date in Julian Calendar
  Calculate Angular Velocity:
  Calculate Mean Anomaly:
  Solve For eccentric Anomaly:
  Find Polar Coordinates:
  Convert to Geocentric Equatorial Coordinates:
  Convert to Rotating Rectangular Coordinate System:
Notes: Mu: kepplers constant

## Slide 9: Computing SSP
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
  Sub-Satellite Point
    Point on earth’s surface directly beneath a satellite.
    Expressed in terms of latitude and longitude
    Computed using the satellite’s coordinates in the rotational coordinate system
Latitude
Longitude
Notes: Mu: kepplers constant

## Slide 10: Lookup Angles
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
  Elevation & Azimuth Angle:
    Needed for pointing the Ground Station to target Satellite (UL & DL)
    Used for computing path loss
Lookup Angles Computation | 
Elevation | Azimuth
 | Case-1: At-least one point (SSP or ES) is in Northern Hemisphere Case-2: Both points are in the Southern Hemisphere
Lookup Angles Computation | 
 | Azimuth
 | Case-1: At-least one point (SSP or ES) is in Northern Hemisphere Case-2: Both points are in the Southern Hemisphere
Notes: Re_ radius of earth
R_s – distance to satellite

## Slide 11: Channel Model
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
The values for the absorption losses are obtained from the ITU Recommendation ITU-R P.676-12 as well as Recommendation ITU-R P.835.
Select Source GS
Get latitude, longitude, and altitude of GS
Compute Potential Satellites in the FOV of GS [Visibility Test]
Select Satellite With Shortest Distance to GS
Using Computed Satellite SSP at Time (t) Compute GS Inclination Angle
Compute Atmospheric Profile Using P.835 or Use API Call to Retrieve Accurate Atmospheric Profile of GS at Time (t) (Supported Functionality in weather.py – API Key Provided)
Compute Molecular Based Attenuation and Spreading Loss
Notes: Mu: kepplers constant

## Slide 12: Link Budget
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
Highest Achievable Modulation Scheme Given BER
THz Band |  |  | 
 | UL | DL | CL
Frequency [GHz] | 217.5 | 295 | 295
Bandwidth [GHz] | 17 | 40 | 40
Satellite Gain [dBi] | 45 | 48 | 48
Terminal Gain [dBi] | 49 | 72 | -
TX Power [mW] | 200 | 200 | 200
Ka Band |  |  | 
 | UL | DL | CL
Frequency [GHz] | 28.75 | 40 | 26.375
Bandwidth [GHz] | 2.5 | 5 | 2.25
Satellite Gain [dBi] | 28 | 30 | 27
Terminal Gain [dBi] | 52 | 54 | -
TX Power [mW] | 5000 | 5000 | 5000
Notes: Mu: kepplers constant

## Slide 13: Routing
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
To fully capture network performance, latency needs to be computed
A routing protocol needs to be programmed in the simulation
  Not many options were available
  Most routing protocols are proprietary (ex. Starlink)
Our base routing model was a simple shortest first hop algorithm
The first satellite is picked based on shortest distance to source ground station
The last satellite is picked based on shortest distance to target ground station
Each hop needs to move in the direction towards destination
With mega-constellations, there will be numerous options to pick in the cross-link
Methodologies:
  Pick the shortest-range hop to maximize data-rate
    Could lead to zig-zag pattern and not a “straight path” to destination
  Pick the longest-range hop to minimize overall latency and route distance
    Might reduce the MCS leading to a higher transmission time
Process:
  Select UL and DL Satellite
  At each hop:
    Conduct visibility test (SAT to SAT)
    Conduct LB test
  Select longest range hop in the direction of destination
Notes: Mu: kepplers constant

## Slide 14: Routing
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
Process:
  Select UL and DL Satellite
  At each hop:
    Conduct visibility test (SAT to SAT)
    Conduct LB test
  Select longest range hop in the direction of destination
Assumptions:
  TX & RX Antennas are perfectly aligned
  No blockages caused by other satellite or objects in space
  Satellites maintain location during routing (avoids excessive computations)
  No MAC overhead
Alternatives:
  Brute Force:
    Compute all possible routes, and select the one with lowest latency
    Very time consuming in mega-constellations.
Notes: Mu: kepplers constant

## Slide 15: Routing
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
Mega-Constellation: 3-Hop Relay (29.6ms latency)
Notes: Mu: kepplers constant

## Slide 16: Routing
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
15 Satellites: 3-Hop Relay (52.3 ms latency)
Notes: Mu: kepplers constant

## Slide 17: Simulation Ecosystem
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
To compare THz and KA performance, we ran a simulation:
  Transmission times are modeled as Poisson Process
  Simulation time duration is set to 4 hours
  The source and destination ground stations are picked at random from a list of 11 cities
    Ex: Fresno-California, Raleigh-North Carolina, Moscow-Russia, Izmir-Turkey, Nairobi-Kenya, …
    The elevation of these cities are taken into account during the path-loss calculation.
  Number of Satellites: ~4000 [custom built constellations – supported by simulator]
  Satellite Altitude: 300km
Notes: Mu: kepplers constant

## Slide 18: Results: KA Band
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
Notes: Mu: kepplers constant

## Slide 19: Results: THz Band
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
Notes: Mu: kepplers constant

## Slide 20: Results: Hybrid
Sub-THz Software-Defined Radio (SDR) Implementation
Medium Access Channel (MAC) Protocol
Digital / Analog Hybrid Solution
8/10/20 GHz Options
RFSoC: ZU28DR GEN 1
Technology
16-nm FinFET
RF
8 DACs , 8 ADCs
Alternative
JESD to Ext.
DSP{4K}, LUTS{930k}
Processing System
ARM A53, ARM R5
Application
mmWave
Programmable Logic
Notes: Mu: kepplers constant

## Slide 21: Results: Propagation Delay

## Slide 22: Conclusion